## Slide 1
Closed-Loop Soundboard Design Using GPU-Accelerated Modal Synthesis and Physical Verification
A quantified design-fabrication-verification methodology for piano soundboards
Co-Development Proposal: Industry + University
PIANOID

## Slide 2
The Problem
Why do some pianos sing while others stay dull — and why can’t we answer this systematically?
Systematic soundboard design is economically and methodologically impossible with current tools. A concert grand has 230 strings coupled through thousands of resonance modes. Evaluating one design change requires weeks of labor and thousands in materials. • “Killer octave” — poor sustain in 5th–6th octave. Mechanism understood; design solution is not • Design knowledge exists as intuition, not transferable parameters
Research Question
Can a closed-loop methodology — FEA design, real-time preview, fabrication, and quantified modal verification — make soundboard design systematic and reproducible?
Core Experiment
A/B synthesis: FEA-predicted modes vs. physically measured modes on the same engine. Isolates model accuracy from synthesizer fidelity. If predicted and measured soundboards converge perceptually, the design loop is validated.

## Slide 3
An Actively Explored Field
Group
Focus
Key Contribution
Chabassier, Chaigne (Inria/ENSTA)
FE simulation
Energy-preserving string+soundboard+air (JASA 2013)
MAESSTRO (ANR)
Soundboard CAD
FEA modal synthesis; offline single-note (Acta Acustica 2022)
Ege, Boutillon (Polytechnique)
Modal analysis
Soundboard characterization at manufacturing stages (2018)
Välimäki, Bank (Aalto/Budapest)
Real-time models
Digital waveguide/IIR with psychoacoustic tuning
Modartt Pianoteq
Commercial
~1000 modes/note, proprietary, no design pipeline
Weinreich (Michigan)
String coupling
Coupled polarization and double decay (JASA 1977)
The gap: No work closes the loop from FEA modes through real-time polyphonic synthesis to quantified physical verification. The A/B synthesis experiment — comparing predicted and measured modes on the same engine — has never been performed.

## Slide 4
What Already Exists: The Pianoid Platform
Working System (demonstrated at NAMM)
• GPU modal synthesis — 256 soundboard modes coupled to all strings, real-time on 4070 Ti, 30–50% margin • Inter-string coupling via feedin/feedback matrices (how each mode is energised by strings and returns energy). Sympathetic resonance emerges • Modal measurement — ESPRIT extraction + automated tracking, 78+ positions • Excitation prototype — 8-channel actuators on real soundboard
What This Proposal Builds
• Engine: 256 → 2048 modes — 5000+ shaders available. Challenge: coupling at scale. Approach: flatten coefficients for higher modes. ~2 months. Fallback: 256-mode model • FEA import pipeline — feedin/feedback matrices from FEA eigenmode output • Perceptual validation — ABX listening tests, comparative evaluation

## Slide 5
State of the Art — And Its Gaps
Capability | MAESSTRO | Pianoteq | Pianoid (current) | Pianoid (proposed)
Synthesis speed | 16 min/note | Real-time | Real-time 48kHz | Real-time 48kHz
Polyphony | Single note | Full | 256 strings | 256 strings
Multi-string coupling | No | Proprietary | 256 modes | 2048 modes
Soundboard from FEA | Yes | Hand-tuned | Measured only | FEA-derived
Modal measurement | No | No | ESPRIT pipeline | ESPRIT pipeline
Design verification | No | No | Not yet | A/B synthesis
Acoustic performance | No | No | 8-ch prototype | Multi-point
Blue = proposed capabilities this project delivers.

## Slide 6
Why This Methodology Requires a New Platform
A closed-loop methodology cannot use a conventional piano. Its constraints prevent systematic soundboard variation.
Conventional Piano Framework
• String tension is the primary constraint — 15–20 tonnes defines everything • Weight, shape, size consequential to string tension • Designer works in a space already defined by structural constraints • Swapping a soundboard requires weeks — iteration impractical
Pianoid Enables Iteration
• No permanent string tension — electromechanical excitation, GPU physics • Free exciter placement — actuators anywhere on soundboard • Soundboard swappable — free mounting, no stress. New design in hours • Geometry determined purely by acoustic goals

## Slide 7
The Closed Loop
FEA Design
→
GPU Preview
→
Fabrication
→
Measurement
→
A/B Evaluation
←———— Correlation below threshold? Revise FEA and iterate ————→
Loop closure: quantified modal correlation (frequency, MAC, damping) defines go/no-go. A/B perceptual test validates convergence.
Phases 1–2: Design & Preview
FEA eigenvalue analysis. Per mode: frequency, quality factor, modal mass, mode shape amplitudes at excitation positions. Mode shapes define feedin/feedback coupling matrices.
Phase 3: Fabrication
Reduced-scale test boards. Spruce, plywood, composites. CF ribs are a hypothesis to test.
Phase 4: Modal Verification
ESPRIT + automated tracking. FEA-vs-measured: frequency, MAC (Modal Assurance Criterion), damping.
Phase 5: A/B Synthesis & Evaluation
Core experiment: same engine, FEA vs measured modes. Isolates model accuracy. ABX tests, expert assessment.

## Slide 8
Co-Development: Industry + University (partner TBD)
Pianoid Brings
• GPU modal synthesis engine (working) • Excitation system (8-ch prototype) • Modal measurement pipeline • FEA import tool development • Engine scaling R&D (256→2048)
University Brings
• FEA expertise (orthotropic materials, mesh convergence) • Music perception science (ABX, psychoacoustics) • Prototyping & testing facilities • Acoustic radiation analysis • Credentialing in acoustics community
IP: commercial technology retained by Pianoid. Publications and datasets fully open. Terms negotiated jointly.

## Slide 9
Why Now?
Technology Convergence
• GPU crossing the threshold — 2048-mode real-time modal synthesis feasible for the first time • MAESSTRO laid FEA groundwork — missing: real-time + verification loop • Modal analysis tools mature — ESPRIT extracts hundreds of modes reliably
Platform Readiness
• Pianoid demonstrated publicly — extends a working system • Closed-loop now executable — required combination unavailable 5 years ago
Growing Demand
• Sustainable materials need acoustic evaluation tools • Digital twin expanding from aerospace to acoustics

## Slide 10
Timeline and Risks
Timeline (12 months)
Phase | Mo | Deliverable
Engine scaling | 1–2 | Validated (or fallback)
FEA import | 1–3 | Working pipeline
FEA design | 2–5 | Modal basis, 2+ designs
GPU preview | 4–6 | Virtual instruments
Fabrication | 4–8 | Test boards
Measurement | 7–9 | FEA-vs-measured
A/B evaluation | 8–11 | ABX, prototype
Publication | 10–12 | Papers, dataset
Key Risks
2048-mode scaling fails
Fallback: 256-mode model. Next-gen NVIDIA adds headroom.
Poor FEA correlation
Start simple. Discrepancies inform refinement — this is the research.
Prototype validity
Spruce baseline alongside experimental materials.
Partnership timeline
Parallel workstreams; industry work proceeds independently months 1–3.

## Slide 11
Expected Outcomes
Scientific
• Validated closed-loop methodology with go/no-go criteria • A/B synthesis results — controlled FEA vs measured • Design guidelines — sensitivity of acoustic features to structural parameters • Open modal dataset
Publications
• Closed-loop methodology + A/B results (Acta Acustica) • Mode tracking methodology • Hybrid instrument: concept + evaluation
Technological
• Playable prototype — soundboard + excitation, live performance • Software pipeline — FEA-to-engine import • Modal measurement toolkit
Industrial
• Computer-aided soundboard design with real-time preview • Sustainable materials evaluation pathway

## Slide 12
The first system that lets you hear a soundboard before you build it — and verify what you built against what you designed.
PIANOID